## Slide 1
GHOSTPRINT
IoT device identification via network-traffic fingerprinting
RAIoT Lab — Amity University Rajasthan · Innovation Day 2026
WHAT IT IS
GhostPrint identifies the IoT devices on a local network from how they communicate — packet sizes, inter-packet timing, packet rate and burstiness — not from what they transmit. A Random Forest classifies each device from a 12-second behavioural window and never reads a payload byte, so identification works identically on encrypted traffic. Two anomaly detectors flag rogue devices and impersonation (spoofing) attacks in real time.
HOW IT WORKS
1 · Simulate
3 ESP8266 profiles + rogue & spoofer boards, or the software twin
2 · Capture
UDP metadata only: size, timing, source IP
3 · Fingerprint
12 s rolling window → 4 behavioural features
4 · Classify
Random Forest: label + confidence score
5 · Detect & show
rogue / spoofing alerts → live dashboard
THE BEHAVIOURAL FINGERPRINT
One 12-second window per device yields four features. The three demo profiles sit far apart in this space:
Device | Avg packet size | Inter-packet interval | Packets / min | Burstiness
SensorNode | 72 B | 5,000 ms | 12 | 0.08
CameraStream | 1,200 B | 33 ms (in-burst) | 55 | 0.24
SmartSwitch | 32 B | 1,800 ms | 33 | 0.50
Source: GhostPrint device profiles (config.py) — the same profiles generate the training corpus.
ATTACK DETECTION
ROGUE DEVICE
An unknown device joins the network: its feature vector sits far from every known device profile (scale-aware z-distance), or the classifier is unconfident. Amber warning naming the source IP.
Alert in ≤ 5 s
SPOOFING ATTACK
An impostor takes over a known device's identity: a gated per-device z-score baseline spots the timing drift, and attack traffic never reshapes the reference. Red critical alert naming the victim.
Alert in ~10 s
VERIFIED RESULTS
100%
5-fold CV accuracy
25
automated tests
22
SRS requirements
≤ 5 s
rogue alert
~10 s
spoofing alert
Accuracy: 5-fold cross-validation over the 1,500-window training corpus. Latencies: scripted end-to-end runs (scripts/smoke_test.py replays the full attack scenario headlessly).
RUN THE DEMO
pip install -r requirements.txt
python scripts/run_demo.py
open http://localhost:5000 (no ESP8266 hardware required)
Click Rogue Device for an amber alert in ≤ 5 s; select SensorNode under Spoofing Attack for a red critical alert in ~10 s.
Stack: Python 3.10 · scikit-learn · Flask + Socket.IO · Chart.js · scapy · ESP8266 — thresholds in one config.py.
GhostPrint — research / educational use · RAIoT Lab, Amity University Rajasthan · Innovation Day 2026